## Slide 1
Data Acquisition
Orthophotos & Footprints
Data Processing
512 x 512 Tiling
Rasterization
Mask Filtering
Class Weighting
Model Development
Multi-Class U-Net
Weighted SCCE + Dice Loss
Model Training
70% Training & 30% Validation
Callback & Optimization
Model Evaluation
Accuracy & Spatial Metrics
Error Map Analysis
Development
Batch Inference Pipeline
GIS Integration
Scaling & monitoring
Regional Expansion
Periodic Model Retraining

## Slide 2
Road
map
Of the Project
Data Acquisition & Preparation
Model Development & Optimization
Model Validation & Evaluation
Model Testing & Retraining
Deployment & Integration
Scaling & Maintenance

## Slide 3
Values | Class | No. of Pixels per class
0 | Background | 216012504
1 | RCC Roof | 93348733
2 | Tiled Roof | 323656
3 | Tin Roof | 16563012
4 | Other Roofs | 3791391
Features Class Distribution in Training Dataset
As per features class distribution, Background noise is very higher throughout the dataset. To overcome this class imbalance, inverse frequency class weights are defined
Class | 0 | 1 | 2 | 3 | 4
Weights | 0.006749 | 0.0156196 | 4.50502233 | 0.0880321 | 0.3845758